Code 42: Advanced protective packaging for

Colour coated coils local & export

- Circumferential strap

- Galvanised cover plate strapping 0.9 mm x 32 mm

- Seal of circumferential strap

- Seal protector

- Masonite strips

<925mm = 2 strips

≤1 200 mm = 3 strips

>1 200 mm = 4 strips

- Seal

- VCI paper

- Circumferential strap applied over masonite

- ArcelorMittal Logo and dispatch sticker

- Eye ring

- Eye tie

- Open top hat

- Outer corner bracket

- Moisture indicator (2 stickers per coil, on both ends)

Corrosion considerations

- Packaging classified as Advanced Protective has a masonite strip on circumference and cover sheet.

- Although advanced, the packaging is not fully airtight which implies that coils must be appropriately protected against rain and wetness during loading, transit and off-loading.

- To prevent condensation and premature deterioration of strip surface condition, the coils must be stored in a dry, ventilated warehouse.

Corrosion guarantee

| Description | Product code | SPE | * Allowed claim period per surface treatment |
| --- | --- | --- | --- |
|  |  |  | None | Passivated | Dos oil | Rust preventative oil |
| Textradek® CR/Textradek® Galv, Chromadek® , Chromaprep® | DCC, DGC, KGC, PGC | 135/145 | 120 | n/a | n/a | n/a |

* Days after receipt of material.

n/a- not available/applicable

Note:

- Claims for corrosion will only be considered by Mittal Steel South Africa if the material has been properly stored in a dry, ventilated warehouse, and the claims submitted within the periods indicated above,

- Once protective packaging has been removed and material taken into stock, Mittal Steel South Africa  will not consider any claims for corrosion.

# Text boxes

Packaging specification: 42

Horizontally Packed Advanced Protective Packaging without Paper